## Slide 1: Adaptive FEC for Congestion Control
Varun Singh, Marcin Nagy, Jörg Ott, Lars Eggert
IETF 91, Honolulu,
09. November 2014
https://tools.ietf.org/html/draft-singh-rmcat-adaptive-fec-01

## Slide 2: IPR
2 IPR disclosures
  Nokia
  Polycom

## Slide 3: Error Resilience
FEC
SSA: Adaptive packet sizes
RPS: reference picture selection

## Slide 4: CONCEPT
RTCP Interval
time
Throughput
media rate
FEC
STAY state
PROBE state
STAY state
STAY state
UP state
UP state
DOWN state
PROBE state
(A) Adding FEC
(B) Swapping FEC with media
(C) Partially swapping FEC with media
Available Capacity

## Slide 5: CC Framework
Media Encoder
Rate Controller
RTP Packets
Transport Layer (UDP)
IP
Source RTP
RTCP FB
Pacing Buffer

## Slide 6: RFC 6363: FEC Framework
Media Encoder
Rate Controller
RTP Packets
FEC Code
FEC Module
RTP (De)mux
Transport Layer (UDP)
IP
Repair RTP
RTCP FB
Source RTP

## Slide 7: State Machine
STEADY
PROBE
DECREASE
INCREASE

## Slide 8: FEC Scheme
Currently, using
  parity, 1- or 2-d interleaved XOR (for burst loss)
  There is discussion in RTCWEB on FEC schemes.
But,
  It could be applied to other schemes
S, Holmer, et al., "Handling Packet Loss in WebRTC", Proc. of IEEE International Conference on Image Processing (ICIP 2013) , 9 2013.

## Slide 9: RTCP Feedback
RLE of Post-repair (RFC5725)
RLE of loss packets (RFC3611)
RLE of discarded packets (RFC7097)
Packet count of lost and repaired packets
  (draft-ietf-xrblock-post-loss-repair)

## Slide 10: Calculating goodput
Receiver reports goodput:
  Goodbytes in reporting interval =
  bytes received – bytes discarded
  OR
Sender calculates goodput:
  Goodbytes in reporting interval =
  bytes sent – bytes lost – bytes discarded
RLE reports

## Slide 11: Undershoot
Congestion reported
  Sender calculates duration of congestion =
    HSN when RTCP scheduled – HSN when congestion detected
  undershoot bytes = sending rate * duration/8
  New rate = Goodbytes – undershoot bytes [1]
              OR
  Delta = Sending rate – goodput
  New rate = sending rate – 2 x delta [2]
[1] http://www.netlab.tkk.fi/~jo/papers/2012-videv-rate-control.pdf
[2] http://www.netlab.tkk.fi/~varun/nagy2014mmsys.pdf

## Slide 12: Typical results
~90% recovery in time for decoding when FEC interval was short
  Fewer packets protected
~80% recovery in time for decoding when FEC interval was long
  More packets protected

## Slide 13: Applicability
Implemented over a delay-based congestion control
  See paper for details
However would like to generalize it.
  Apply to SCReAM, GCC, …
  Nagy M., Singh V., Ott J., Eggert L., Congestion Control using FEC for Conversational Multimedia Communication, Proc. of ACM Multimedia Systems, Singapore, SG, Mar, 2014,

## Slide 14: Evaluation (1/3)
Ns-2 simulation, Variable link capacity, Single flow on the link
OWD: 50ms
Notes: Variable link capacity 1 graph to show (undershooting and bounceback to discuss)
Dummynet graph to show

## Slide 15: Evaluation (2/3)
OWD: 100ms

## Slide 16: Evaluation (3/3)
OWD: 240ms

## Slide 17: 50ms

## Slide 18: 50ms

## Slide 19: 100ms

## Slide 20: 100ms

## Slide 21: RTT fairness (50ms)

## Slide 22: 5.4: RTT fairness

## Slide 23: RTT fairness (100ms)

## Slide 24: RTT fairness (100ms)

## Slide 25: Compete with short TCPs

## Slide 26: TESTBED Evaluation (1/2)
1Mbit/s link capacity, 50ms one-way-delay,
Two RTP flows on the link
Notes: Variable link capacity 1 graph to show (undershooting and bounceback to discuss)
Dummynet graph to show

## Slide 27: TESTBED Evaluation (2/2)
1Mbit/s link capacity, 100ms one-way-delay,

## Slide 28: Next steps
Code: (coming soon)
  https://github.com/protocols-comnet/rmcat-adaptive-fec-code
Evaluation Paper:
  Nagy M., Singh V., Ott J., Eggert L., Congestion Control using FEC for Conversational Multimedia Communication, Proc. of ACM Multimedia Systems, Singapore, SG, Mar, 2014,
More feedback is appreciated 